## Slide 1: EECS 489 Computer Networks Winter 2023
Z. Morley Mao
Material with thanks to Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
CDN: Content Distribution Network
DNS: Domain Name System

## Slide 3: Recap: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent (latency)
  Parallel/concurrent (bandwidth and latency)
  Pipelined over the same connection (latency)
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 4: Replication
Replicate popular Websites across many machines
  Spreads load across servers
  Places content closer to clients
  Helps when content isn’t cacheable

## Slide 5: Content Distribution Networks (CDN)
Caching and replication as a service
Large-scale distributed storage infrastructure (usually) administered by one entity
  e.g., Akamai is in 130 countries and 1700 networks
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 6: Cost-effective content delivery
General theme: multiple sites hosted on shared physical infrastructure
  Efficiency of statistical multiplexing
  Economies of scale (volume pricing, etc.)
  Amortization of human operator costs
Examples:
  CDNs
  Web hosting companies
  Cloud infrastructure

## Slide 7: CDN example – Akamai
Akamai creates new domain names for each client
  e.g., a128.g.akamai.net for cnn.com
The client content provider modifies content so that embedded URLs reference new domains
  “Akamaize” content
  e.g., http://www.cnn.com/image-of-the-day.gif becomes http://a128.g.akamai.net/image-of-the-day.gif
Requests now sent to CDN’s infrastructure

## Slide 8: CDN example – Akamai
Retrieved on Sep 10, 2021 from https://www.akamai.com/visualizations/media-delivery-network-map

## Slide 9: Why direct clients to particular replicas?
Balancing load across server replicas
Pairing clients with nearby servers to decrease latency and overall bandwidth usage

## Slide 10: DNS: Domain name system

## Slide 11: Internet names & addresses
Machine addresses: e.g., 141.212.113.143
  Router-usable labels for machines
  Conforms to network structure (the “where”)
Machine names: e.g., cse.umich.edu
  Human-usable labels for machines
  Conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other
  A directory service

## Slide 12: Why?
Convenience
  Easier to remember
Provides a level of indirection!
  Decoupled names from addresses
  Many uses beyond just naming a specific host

## Slide 13: DNS: History
Initially all host-address mappings were in a hosts.txt file (in /etc/hosts):
  Maintained by the Stanford Research Institute (SRI)
  Changes were submitted by email and updates downloaded periodically from SRI
As the Internet grew SRI could not handle load
  Names were not unique anymore
  Hosts had inaccurate copies of hosts.txt

## Slide 14: DNS: History
In 1983, the first stable operational DNS implementation included
  The associated query protocol;
  A server implementation; and
  Initial root servers.
Since inception, DNS scaled from 1000s of queries/day to 10s of billions queries/day

## Slide 15: Goals
Uniqueness: no naming conflicts
Scalable
  Many names and frequent updates (secondary)
Distributed, autonomous administration
  Ability to update my own (machines’) names
  Don’t have to track everybody’s updates
Highly available
Lookups are fast
Perfect consistency is a non-goal

## Slide 16: How?
Partition the namespace
Distribute administration of each partition
  Autonomy to update my own (machines’) names
  Don’t have to track everybody’s updates
Distribute name resolution for each partition
How should we partition things?

## Slide 17: Key idea: Hierarchy
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 18: Hierarchical namespace
“Top Level Domains” are at the top
Domains are subtrees
  e.g., .edu, umich.edu, eecs.umich.edu
Name is leaf-to-root path
  cse.eecs.umich.edu
Depth of tree is arbitrary (limit 128)
Name collisions trivially avoided
  Each domain is responsible
root
edu
com
gov
mil
org
net
uk
fr
umich
berkeley
eecs
law
cse
…

## Slide 19: Hierarchical administration
root
edu
com
gov
mil
org
net
uk
fr
umich
berkeley
eecs
law
cse
…
A zone corresponds to an administrative authority that is responsible for that portion of the hierarchy
  e.g., UMich controls names: *.umich.edu
  e.g., EECS controls names: *.eecs.umich.edu
ICANN/IANA
Notes: ICANN: Internet Corporation for Assigned Names and Numbers
IANA: Internet Assigned Numbers Authority

## Slide 20: Server hierarchy
Top of hierarchy: Root servers
  Location hardwired into other servers
Next Level: Top-level domain (TLD) servers
  .com, .edu, etc.
  Managed professionally
Bottom Level: Authoritative DNS servers
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority

## Slide 21: Server hierarchy
Each server stores a (small!) subset of the total DNS database
An authoritative DNS server stores “resource records” for all DNS names in the domain that it has authority for
Each server needs to know other servers responsible for other portions of the hierarchy
  Every server knows the root
  Root server knows about all top-level domains

## Slide 22: DNS root
Located in Virginia, USA
How do we make the root scale?

## Slide 23: 13 DNS root servers
https://root-servers.org/

## Slide 24: 5-minute break!

## Slide 25: Announcements
Midterm Wed Feb 22 2023
  9AM
Assignment 1 due Fri Jan 27, 2023, 11:59 PM.

## Slide 26: DNS records
DNS servers store resource records (RRs)
  RR is (name, value, type, TTL)
Type = A: ( Address)
  name = hostname
  value = IP address
Type = NS: ( Name Server)
  name = domain
  value = name of DNS server for domain

## Slide 27: DNS records (cont’d)
Type = CNAME: ( Canonical Name)
  name = alias name for some “canonical” (real) name
    e.g., cse.umich.edu is really cse.eecs.umich.edu
  value = canonical name
Type = MX: ( Mail eXchanger)
  name = domain in email address
  value = name(s) of mail server(s)

## Slide 28: Inserting Resource Records into DNS
Register foobar.com at registrar
  Provide registrar with names and IP addresses of your authoritative name server(s)
  Registrar inserts RR pairs into the .com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.44.9.129, A)
Store resource records in your server dns1.foobar.com
  e.g., type A record for www.foobar.com
  e.g., type MX record for foobar.com

## Slide 29: Using DNS (Client/App View)
Two components
  Local DNS servers
  Resolver software on hosts
Local DNS server (“default name server”)
  Clients configured with default server’s address OR learn it via a host configuration protocol (e.g., DHCP)
Client application
  Obtain DNS name (e.g., from URL)
  Do getnameinfo() to trigger DNS request to its local DNS server
Notes: DHCP: Dynamic Host Configuration Protocol

## Slide 30: dig
dig nyu.edu
; <<>> DiG 9.10.6 <<>> nyu.edu
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 47443
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 512
;; QUESTION SECTION:
;nyu.edu. IN A
;; ANSWER SECTION:
nyu.edu. 60 IN A 216.165.47.10
;; Query time: 39 msec
;; SERVER: 192.168.1.1#53(192.168.1.1)
;; WHEN: Fri Sep 10 08:21:43 EDT 2021
;; MSG SIZE rcvd: 52

## Slide 31: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 32: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 33: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 34: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 35: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 36: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 37: Two ways to resolve a name
Recursive name resolution
  Ask server to do it for you
Iterative name resolution
  Ask server who to ask next
The iterative example we saw is a mix of both!

## Slide 38: DNS protocol
Query and Reply messages; both with the same message format
  Header: identifier, flags, etc.
  Plus resource records
Client–server interaction on UDP Port 53
  Spec supports TCP too, but not always implemented

## Slide 39: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available?

## Slide 40: Reliability
Replicated DNS servers (primary/secondary)
  Name service available if at least one replica is up
  Queries can be load-balanced between replicas
Usually, UDP used for queries
  Reliability, if needed, must be implemented on UDP
Try alternate servers on timeout
  Exponential backoff when retrying same server
Same identifier for all queries
  Don’t care which server responds

## Slide 41: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available
Fast lookups?

## Slide 42: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 43: TTL in dig output
dig nyu.edu
; <<>> DiG 9.10.6 <<>> nyu.edu
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 47443
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 512
;; QUESTION SECTION:
;nyu.edu. IN A
;; ANSWER SECTION:
nyu.edu. 60 IN A 216.165.47.10
;; Query time: 39 msec
;; SERVER: 192.168.1.1#53(192.168.1.1)
;; WHEN: Fri Sep 10 08:21:43 EDT 2021
;; MSG SIZE rcvd: 52
TTL
Notes: 60 Seconds

## Slide 44: Negative caching
Remember things that do not work
  Misspellings like www.google.comm
  These can take a long time to fail the first time
  Good to remember that they do not work so the failure takes less time the next time around
Negative caching is optional
  Not widely implemented

## Slide 45: Important properties of DNS
Administrative delegation and hierarchy enables:
  Easy unique naming
  “Fate sharing” for network failures
  Reasonable trust model
  Caching increases scalability and performance

## Slide 46: DNS provides indirection
Addresses can change underneath
  Move www.cnn.com to 4.125.91.21
Name could map to multiple IP addresses
  Load-balancing (CDN)
  Reducing latency by picking nearby servers (CDN)
  Try out: dig google.com a few times
Multiple names for the same address
  E.g., many services (mail, www) on same machine
  E.g., aliases like www.cnn.com and cnn.com

## Slide 47: Summary
CDNs improve web performance
  Via replication and caching
  Good server selection
DNS allows us to go to webpages without having to memorize IP addresses
  Allows a level of indirection that enables many functionalities including CDN server selection